## Slide 1
Gary Radloff, Sheldon Du, Pam Porter and Troy Runge

## Slide 2: Agenda
Background: Research for WI Energy Office
Quality
  Survey on sample properties
  Impact on conversion limitations
Quantity
  Where is the biomass?
  How much is available? At what cost?
Impact to current business and next steps
Notes: Is this needed?

## Slide 3: Theme and Topics
Planning a transition to new energy economy
Biomass is already WI leading renewable energy source
  Have abundant supply for the future
Biogas leading opportunity: On-Farm AD, Wastewater Treatment Plants AD, and Landfill Diversions and CHP combinations & thermal
Need supportive public policy to achieve success in Wisconsin

## Slide 4: Simplified Conversion Pathways Biomass to Energy/Fuels
Solid Waste
Manure
Grasses & Corn Stover
Wood Residuals
Gaseous fuels
Liquid fuels
Solid fuels
Heat & Power
Anaerobic digestion
Saccharification & fermentation
Pyrolysis / Gasification
Combustion
Transportation
Primary
Secondary

## Slide 5: Wisconsin Biomass Numbers
Biomass Type / Estimate methodology | Million Dry Tons/year
Corn Stover Estimates | 
NASS Data | 2.81
BTS Data@$60/MT | 2.49
Wood Residuals | 
TPO Roundwood | 1.29
TPO Harvest residuals | 1.52
Energy Crops | 
BTS Woody@$60/MT | 2.29
BTS Grasses@$80/MT | 0.15
WBA Fallow Hay/CRP | 3.13
Manure | 
NASS Dairy Aus | 4.77
Notes: Showing general number with different data source estimates

## Slide 6: Biomass Opportunities
Identified top counties with biomass densities
Looked for natural groupings
Used circles to identify processing sites >200,000 tons/year

## Slide 7: Quality - Biomass Analyses
Proximate Analysis
  Moistures, Volatile Matter, Fixed Carbon, Ash
Heating Value
Ultimate Analysis
  C, H, N, O, S
Cl, Hg, Mineral Ash Analysis
Crude Protein
Carbohydrate
Lignin
Notes: Is this needed?

## Slide 8: Identified Thermal Conversion Issues
Fuel Characteristic | unit | Woody | Herbaceous | Residuals
Moisture | (% wt wb) | 2.74% - 49.94% | 2.45% - 18.32% | 6.96% - 28.62%
LHV | Btu/lb | 3200 - 8946 | 5926 - 6923 | 5019 - 8145
Ash | (% wt db) | 0.63% - 9.33% | 2.66% - 10.83% | 5.21% - 19.38%
N | ppm db | 200 - 10200 | 3700 - 15500 | 2500 - 42700
S | ppm db | 110 - 670 | 370 - 3130 | 1400 - 8590
Cl | ppm db | 19 - 617 | 293 - 6516 | 786 - 12550
Hg | ppm db | <0.001 - 0.024 | <0.001 - 0.017 | <0.001 - 0.027
Fouling Index | lb alkali/MMBtu | 0.099 - 1.471 | 0.227 - 1.919 | 0.314 - 1.482

## Slide 9: Quality Summary
Link known technologies with Biomass based on quantity
Thermochemical  Woody & Woody Waste
  Combustion
  Gasification
Biological  Herbaceous & Herbaceous Waste
  Fermentation
  Anaerobic digestion

## Slide 10: Biomass Opportunities
Manure assumed to be on CAFOs

## Slide 13: Woody Biomass Economic Scenarios
Residuals and pulpwood markets
  RPS demand for woody biomass
  Biofuel feedstock demand
  Pulpwood demand from pulp/paper industry
  Mill capacity expands or contracts by 10%
Potential overlaps
  High bioenergy demand
  Expanding pulp/paper markets

## Slide 14: Analysis Framework-Scenarios
Price
Quantity
Residue
Pulpwood
Sawlogs
Bioenergy demand (RPS, RFS…)
Pulp/Paper industry demand

## Slide 15: Impact to Existing Industry
Most developed biomass industry is forest products
Wisconsin has a large pulp & paper industry
What would the impact of increased woody biomass demand be?
Roundwood (MCF) | Sawlogs | Pulpwood
360.8 | 98.2 (27%) | 250.8 (70%)
Source: Wisconsin Timber Industry: An Assessment of Timber Product Output and Use in 2003. http://nrs.fs.fed.us/pubs/rb/rb_nrs19.pdf

## Slide 16: Impact on NW Region Pulpwood Market
Chart: Biomass Demand for T-C Conversion (tons)
| 400000.0 | 600000.0 | 800000.0 | 1.0E6
10% pulping capacity decrease | 0 | 21.2892 | 53.5444 | 85.7995
no capacity change | 42.8315 | 65.6441 | 97.8992 | 130.1544
10% capacity increase | 87.1863 | 109.9989 | 142.2541 | 174.5092

## Slide 17: Conclusions
Wisconsin has a large amount of biomass available for bioenergy projects
Pockets of high density biomass create opportunities for aggregation
Woody biomass is only source tested to consistently have quality need for thermal conversion
With a developed forest products industry only wood residuals can be used without impacting regional wood prices
  NW region of WI - 2 plants at 200,000 ton/year each
  NE region of WI - 1 plants at 200,000 ton/year each

## Slide 18: Conclusions Part II
WI should look to investments in waste handling and processing as opportunities for energy production (wastewater treatment, landfills and industrial sites).
Biomass feedstock manure is already aggregated at CAFOs and farms, these are logical energy sites
Small to mid-size thermal is cost competitive today with propane and heating oil. WI can do much more.
Tipping Point for WI: A highly vulnerable economy dependent on global energy or innovative domestic leadership in biogas, thermal, CHP and microgrids.

## Slide 19: Gary Radloff gradloff@wbi.wisc.edu